## Slide 1: AI-Based Smart Traffic Management
Adaptive, emergency-aware and coordinated signal control with YOLOv8 vision and queue forecasting
REVIEW 1 · PROBLEM IDENTIFICATION AND RESEARCH
Presented by
Buneti Harshitha 23K91A0548
Bhuvaneshwari Kadike 23K91A0537
Ambati Sai Nikhil Reddy 23K91A0510
Chapala Rohith Reddy 23K91A0551
Under the guidance of
Laxmi Prasanna, [DESIGNATION]
Department of Computer Science and Engineering
TKR College of Engineering & Technology · Batch A10 (CSE-A) · [ACADEMIC YEAR]
Notes: Introduce the team and the title. One sentence: FlowSense puts vehicle detection, queue forecasting, adaptive signal timing, emergency-vehicle priority and junction-to-junction coordination into one working system, and measures it against fixed-time and emergency-aware baselines.

## Slide 2: Contents
01
Abstract and overview
02
Base paper
03
Literature survey and evidence
04
Existing system and limitations
05
Research gap
06
Problem statement and objectives
07
Proposed approach and architecture
08
Expected outcomes
09
References
Notes: Agenda. This review is about why the problem matters and what is missing in current work; design details and measured results come in the later reviews.

## Slide 3: Abstract: see the traffic, adapt the signals
!
The problem
Traffic congestion raises travel time, fuel use and delay for ambulances. Fixed-time signals cannot react to real traffic, and most systems either detect vehicles or adapt timing, rarely both together with emergency priority.
i
Our idea
One pipeline: YOLOv8 vehicle detection and density, a machine-learning forecast of queues 30 s ahead, adaptive green times, emergency-vehicle priority, coordination between neighbouring junctions and a violation log.
✓
The deliverable
FlowSense: a simulator with four controllers on identical traffic, a vision module, a queue forecaster and a FastAPI + React control console, with delay and ambulance clearance time measured.
Notes: Three points: the weakness of fixed-time and detect-only systems, the idea of one pipeline, and what is delivered. Everything runs locally on a CPU, without a GPU.

## Slide 4: Base paper
M. Lamrabet, M. Alami Chentoufi and R. Ellaia, "Emergency-aware adaptive traffic signal control using YOLO-based light-bar detection and SUMO system-level validation," IEEE Access, vol. 14, pp. 104922-104933, 2026, doi: 10.1109/ACCESS.2026.3710015.
M
Method
A YOLO26m detector, trained on 3,130 annotated images, finds the roof-mounted siren / light-bar (single class). A priority arbitrator (confidence 0.5, 3 consecutive frames) overrides a GA-SGD optimised signal plan and restores it after the vehicle passes.
R
Reported results
Detector: precision 0.73, recall 0.69, mAP50 0.73, 11.45-13.89 ms per frame on a T4. SUMO, one Rabat roundabout: ambulance travel 56 s vs 70 s (GA-SGD) and 64 s (fixed-time); total waiting 19,887 s vs 22,827 s and 33,719 s.
L
Relevance and limits
Same core idea: detect the emergency cue and adapt the signal. The paper itself lists a moderate dataset, simulation-only validation, a single roundabout and no flashing-state check. FlowSense adds forecasting and junction coordination.
Notes: Read the citation. The paper adds a trained light-bar detector to an already optimised controller and shows, in SUMO, shorter ambulance trips and lower total waiting. It is validated on one modelled roundabout in simulation, which is the main limit we try to widen: several junctions, a forecast, coordination.

## Slide 5: Literature survey
Work | Year | Approach | Reported result / limitation
Lamrabet et al. [1] (base) | 2026 | Trained YOLO26m roof light-bar detector as a priority layer over a GA-SGD controller; SUMO roundabout | P 0.73, R 0.69, mAP50 0.73; ambulance trip 56 s vs 70 s (GA-SGD), 64 s (fixed); one roundabout, simulation only
Goenawan (ASTM) [6] | 2024 | YOLOv5 vehicle detection + RNN-LSTM 12-hour count forecast + cycle-length analysis (CARLA) | Forecast MSE 4.521 / RMSE 2.232 vehicles; 21 vs about 15 vehicles/min, 5 s vs about 12 s delay
Gupta et al. [7] | 2026 | Neighbour-embedded graph neural network predicts traffic flow at delivery stations | L1 loss -4.03 %, L2 loss -16.66 %; crowd-delivery focus, no signal control
Lamrabet et al. [8] | 2025 | Hybrid GA-SGD optimisation of signal timing, Moroccan case study | Per the base paper: no emergency-vehicle detection or priority
Sasikala et al. [9] | 2025 | IoT, GPS and RFID emergency prioritisation with dynamic signal control | 35 % shorter ambulance response (as reported in [1]); needs dedicated infrastructure
Zlatkovic et al. [10] | 2023 | Pre-emption concepts for connected-vehicle environments (VISSIM) | Up to 36 % emergency delay reduction (as reported in [1]); needs connected vehicles
Jayakumar et al. [14] | 2024 | Siren recognition from temporal and spectral audio features, SVM and ensembles | 99.5 % accuracy (as reported in [1]); audio has no spatial localisation
Suhana; Satyanarayana; Sharma [18], [19], [20] | 2025 | YOLOv5 / YOLOv8 recognise ambulances, fire trucks and police cars from CCTV | Rely on vehicle appearance, which varies by region and fleet [1]
Signal-IQ [2] | 2026 | Low-cost adaptive control with YOLOv8 vehicle and emergency-vehicle detection (title only) | Hardware-validated per its title; authors and results not verified here
Batch survey [3]-[5] | 2024-25 | Density-based adaptive control; accelerated emergency detection; client-server dynamic control (titles only) | Full texts not accessed; no figures quoted
Notes: The batch survey is the base paper plus four recent works; the ASTM paper is the companion reference. Figures are quoted only where they were read in the paper itself or, marked 'as reported in [1]', from the base paper's own related-work section. For the four survey titles only the title is available, so no results are quoted.

## Slide 6: Supporting evidence: adaptive and priority control pay off
Chart: 
| Fixed-time | GA-SGD | GA-SGD + light-bar priority
Total network waiting time (s) | 33719 | 22827 | 19887
Base paper [1]: SUMO, modelled Souissi roundabout, selected scenario (demand scale 12).
What the literature shows
Adaptive control cuts waiting: 41.0 % lower total waiting than fixed-time in the base paper's scenario [1].
A forecast plus cycle-length control raised throughput from about 15 to 21 vehicles/min in CARLA [6].
Pre-emption reduces ambulance delay: 20.0 % shorter travel than GA-SGD in the base paper [1]; up to 36 % in a VISSIM study reported there.
Reported detector quality is moderate for small light-bars: mAP50 0.73 [1].
Notes: These numbers are the published evidence that motivates the project, taken from the papers we read. They come from different simulators and datasets, so they are not combined or compared with each other. Our own measurements start in Review 2.

## Slide 7: Existing system and current approaches
Cameras / loop sensors
Fixed-time or manual plan
Signal phase per junction
Each junction in isolation
1
Fixed-time and manual control
A fixed cycle gives the same green to an empty approach and a full one. Manual control by police or operators does not scale to a city of junctions. An ambulance waits in the queue like any other vehicle.
2
Adaptive and priority systems
Adaptive timing or vehicle detection is built separately from emergency priority. Priority uses IoT / GPS hardware, audio sirens, vehicle class or a light-bar detector. Neighbouring junctions rarely share what they see.
Notes: Today most junctions run a fixed plan. Where adaptive or priority systems exist, detection, timing, emergency priority and coordination are separate pieces.

## Slide 8: Limitations of existing methods
1
Wasted green time
Fixed timings keep green on empty approaches while queues grow elsewhere, raising delay, fuel use and emissions.
2
Does not scale
Manual control and hand-tuned plans cannot follow demand across many junctions through the day.
3
Emergency delay
Without a priority mechanism, ambulances wait in the queue; IoT and acoustic fixes need extra infrastructure or lose spatial precision.
4
No coordination
Junctions act independently, so clearing one moves the queue to the next; no forecast anticipates the build-up.
The base paper adds: moderate dataset size, light-bar presence only (not flashing state), one roundabout, simulation-only validation [1].
Notes: The first four limitations are the batch problem statement; the last line is the base paper's own limitations section.

## Slide 9: Research gap
1
The surveyed systems perform adaptive signal control or vehicle detection separately: one pipeline that detects, adapts timing, prioritises emergency vehicles and coordinates junctions is missing
2
Emergency priority relies on dedicated infrastructure [9], [10], on audio without localisation [14], or on vehicle appearance [18], [19], [20]
3
The base paper validates one modelled roundabout; it has no queue forecast and no coordination between neighbouring junctions [1]
4
Controllers are rarely compared on identical traffic with the price of pre-emption (delay to other vehicles) measured alongside the ambulance gain
5
Validation stays in simulation for want of authorisation and real-camera trials [1]; transfer of detectors to street cameras is untested
Notes: Gap 1 is the batch survey's own statement. Gaps 2, 3 and 5 come from the base paper's related-work and limitations sections. Gap 4 is our reading: the cost that pre-emption imposes on other traffic is seldom reported next to the ambulance gain.

## Slide 10: Problem statement
Fixed signal timings waste green time on empty approaches while queues build on others
Manual traffic control cannot scale to the number of junctions in a modern city
Emergency vehicles lose critical minutes waiting at signals with no priority mechanism
Junctions operate independently, so clearing one simply moves the queue to the next
Need: a vision-based controller that measures real traffic density, adapts signal timing and gives emergency vehicles priority
Input
Junction camera frames or an uploaded image; simulated demand and ambulance arrivals; road network of 2x2 or 3x3 junctions
Output
Vehicle counts, density level and green-time advice; signal phases; 30 s queue forecast; ambulance pre-emption; violation log
Measures
Average delay per vehicle, queue length, ambulance delay, throughput, fuel wasted idling, detection precision and recall
Notes: Read the statement slowly. The need is a vision-based controller that measures traffic, adapts timing and gives ambulances priority.

## Slide 11: Objectives
1. Ingest live video from junction cameras and detect and count vehicles using a YOLO-based model
2. Estimate traffic density per approach lane from the detection output
3. Compute adaptive signal timings that allocate green time in proportion to measured density
4. Detect emergency vehicles and grant priority passage through the junction
5. Enable coordination between adjacent junctions to smooth traffic along a corridor
6. Evaluate detection accuracy, average waiting time and emergency vehicle clearance time
Validation is in a seeded simulator rather than SUMO; vision is checked on synthetic scenes and on public real photographs.
Notes: The six objectives from the proposal. Later reviews report which were met. We validate on our own simulator because SUMO was not used, and we say so; detection accuracy is reported on real public images as well as synthetic ones.

## Slide 12: Proposed approach
1
Detect
YOLOv8n finds cars, bikes, buses and trucks; a red+blue light-bar rule flags an emergency vehicle; density is counted in passenger-car units (PCU).
2
Forecast
A gradient-boosting model predicts each approach's queue 30 s ahead from 11 features (queue, lags, inflow, signal state, time of day).
3
Control
Green time follows PCU-weighted pressure plus the forecast and arriving platoons; ambulances get a green wave across junctions.
4
Evaluate
Four controllers on identical seeded traffic: fixed-time, adaptive, emergency-aware (base-paper style) and FlowSense advanced.
UI
FastAPI service + React console: live map, benchmark, vision, prediction and violation screens
Violations (red-light, wrong-way) are logged with plate and confidence from simulated events. No database and no GPU are needed.
Notes: Four stages and the console that wraps them. The base-paper-style controller is our emulation of the paper's idea inside the simulator, not a re-implementation of its GA-SGD or its trained detector.

## Slide 13: High-level proposed architecture
Four tiers
Presentation: React and Vite console (port 5310).
Application: FastAPI service (port 8310) with token sign-in and input checks.
Core: traffic simulator with four controllers, queue forecaster, YOLOv8n vision and density.
State: in memory; the model is trained at start-up; no database.
Notes: Follow the diagram top to bottom: the console calls the API, the API calls the simulator, forecaster and vision module. There is no database.

## Slide 14: Expected outcomes and contributions
1
Working platform
A console that runs the simulator live, benchmarks controllers, analyses images, forecasts queues and logs violations.
2
Controller comparison
Delay, queue and fuel compared across four controllers, 2x2 and 3x3 networks, several seeds and demand levels.
3
Emergency priority
Ambulance delay with and without pre-emption, and what pre-emption costs the other traffic.
4
Honest vision check
Vehicle and light-bar detection tested on synthetic scenes and on real public photographs, with failures reported.
5
Stated limits
Simulator not SUMO, no real camera stream, simulated violations: each limit documented, not hidden.
Notes: These are the outcomes we commit to. A first prototype run already shows the adaptive controllers well below fixed-time delay and ambulance delay cut sharply, but those results, and where they are weaker than hoped, are presented in Review 2 and the final review.

## Slide 15: References
[1] M. Lamrabet, M. Alami Chentoufi and R. Ellaia, "Emergency-aware adaptive traffic signal control using YOLO-based light-bar detection and SUMO system-level validation," IEEE Access, vol. 14, pp. 104922-104933, 2026, doi: 10.1109/ACCESS.2026.3710015.
[2] "Signal-IQ: an integrated, low-cost, and hardware-validated adaptive traffic signal control system using YOLOv8-based vehicle and emergency-vehicle detection," 2026 (as listed in the batch literature survey; authors and venue not verified).
[6] C. R. Goenawan, "ASTM: Autonomous smart traffic management system using artificial intelligence CNN and LSTM," arXiv:2410.10929, 2024.
[7] K. Gupta, D. Saxena, A. K. Singh and C.-N. Lee, "Neighbor-embedded graph neural network-based crowd delivery traffic management in smart city," IEEE Trans. Emerg. Topics Comput. Intell., vol. 10, no. 3, 2026, arXiv:2608.22555.
[8] M. Lamrabet, R. Ellaia and M. Alami Chentoufi, "Simulation-based optimization of traffic signals using a hybrid GA-SGD approach: a case study of Morocco," Innov. Infrastruct. Solutions, vol. 10, no. 11, p. 511, Nov. 2025, doi: 10.1007/s41062-025-02319-w.
[9] N. Sasikala, S. Sridhar, S. H. Reddy, S. John and S. Shrinikethan, "Emergency traffic prioritization system with priority-based dynamic route optimization and IoT-enabled dynamic signal control," in Proc. 5th Int. Conf. Intell. Technol. (CONIT), Jun. 2025, pp. 1-5, doi: 10.1109/CONIT65521.2025.11166819.
[10] M. Zlatkovic, Z. Cvijovic, A. Stevanovic and Y. Song, "Concepts of signal control preemption for emergency vehicles in connected vehicle environments," J. Road Traffic Eng., vol. 69, no. 2, pp. 1-7, Jun. 2023, doi: 10.31075/pis.69.02.01.
[14] D. Jayakumar, M. Krishnaiah, S. Kollem, S. Peddakrishna, N. Chandrasekhar and M. Thirupathi, "Emergency vehicle classification using combined temporal and spectral audio features with machine learning algorithms," Electronics, vol. 13, no. 19, p. 3873, Sep. 2024, doi: 10.3390/electronics13193873.
[18] S. Suhana, B. Prathap Rudra, K. Narang and I. Anto, "IoT based emergency vehicle detection using YOLOv8," J. Autom., Mobile Robot. Intell. Syst., vol. 19, no. 2, pp. 79-88, Jun. 2025, doi: 10.14313/jamris-2025-018.x.
[21] J. Redmon, S. Divvala, R. Girshick and A. Farhadi, "You only look once: unified, real-time object detection," in Proc. IEEE Conf. Comput. Vis. Pattern Recognit. (CVPR), Las Vegas, NV, USA, Jun. 2016, pp. 779-788, doi: 10.1109/CVPR.2016.91.
[22] G. Jocher, A. Chaurasia and J. Qiu, "Ultralytics YOLOv8," version 8.0.0, 2023. [Online]. Available: https://github.com/ultralytics/ultralytics
Notes: Selected references; the complete numbered list, with notes on how each entry was checked, is in the project report.

## Slide 16: Thank you
Questions and suggestions are welcome.
Notes: Likely questions: why a simulator instead of SUMO (self-contained, seeded, identical demand for every controller); why YOLOv8n and an HSV light-bar rule instead of a trained light-bar model (no light-bar dataset was trained; real-photo results are reported honestly); how the base paper differs (trained detector, GA-SGD, one roundabout).